Lab 02 Report
Muhammad Hassan Shahid: ms10290
Muhammad Saad Malik: mm10357

Task 0

Task 01

Task 02

Task 03

Task 04

Task 05

## Evaluation Questions:
1. Role of USART2
USART2 on the STM32F3 Discovery board is a peripheral used for UART communication (asynchronous serial communication). It provides the interface for sending and receiving serial data between the STM32 microcontroller and external devices such as a PC or USB-UART module.
UART Mode: Allows asynchronous transmission and reception without a clock signal.
Pins:
PA2 → USART2_TX (Transmit)
PA3 → USART2_RX (Receive)
Function:
TX (Transmit): Sends data from the STM32 to the external device.
RX (Receive): Receives data from the external device into the STM32.
Use Case: Commonly used for debugging, logging, or command/control communication via a USB-UART interface.

2. Why TX and RX Lines Must Be Crossed
When connecting the STM32F3 board to another UART device (like a USB-UART module), the transmit and receive lines must be crossed to ensure proper communication:

STM32 Pin	Function	USB-UART Pin
TX	Transmit	RX
RX	Receive	TX

Reason: Each device’s transmit line must connect to the other device’s receive line.
If TX and RX are not crossed, both devices could be transmitting on the same line or trying to receive from an inactive line, causing communication failure.
Connection Summary:
STM32_TX ↔ USB-UART_RX
STM32_RX ↔ USB-UART_TX
This ensures proper two-way UART communication between the STM32F3 and the USB-UART module.